## Slide 1: IBM Watson Build Challenge
  https://www.ibm.com/partnerworld/wps/static/watsonbuild/
  Team: New York Power Authority, Starboard (consulting), and RPI (J. Chow, M. Wang, L. Vanfretti, Q. Ji)
  Selected in Phase 1; now in Phase 2 competition (due Oct. 2017)
  Proposal: develop cognitive solutions to power system control room operation, including alarming processing and control augmentation, by linking cognitive processing of warning messages and technical analysis of various sources of power system data
    The cognitive processing part will rely on Watson APIs
    Power system data analysis will be based on technical tools developed by the RPI team

## Slide 2: Cognitive Solutions to Power System Control Room Operation
Rank the exceeding limits events
Streaming Data
Warning Message
Watson Retrieve and Rank
API
Whether are there events exceeding limits?
RPI Data Analysis
Missing Data Recovery
Static Overload Testing
Disturbance Recognition
Data Science Experience
Control Room

## Slide 3: Alarming Processing
Raw warning messages
Document Conversion
Training
of Retrieve and Rank
Testing
of Retrieve and Rank
Question:
Response:

## Slide 4: Control Augmentation
Three Data Analysis algorithms are implemented on IBM Data Science Experience
  Online Missing Data Recovery
  Static Overload Testing
  Disturbance Recognition

## Slide 5: Online Missing Data Recovery
Functions:
To recover the missing data of phase measurement units (PMU) streaming data
Input:
PMU streaming datasets;
Output:
The reconstructed PMU streaming datasets.
Fig. 1 is the reconstructed results.
Fig. 1: Voltage magnitudes and current magnitudes after a dicturbance

## Slide 6: Static Overloading Testing
Functions:
To check whether the operational limit of the transmission lines has been breached.
To check whether steady state is reached.
Overload index:
Where is the overload performance index for the operating point ;
is the number of transmission lines;
and are the average and maximum power flows of the th line;
is a weighting factor for each transmission line;
The of the case in Fig. 2 is 1.28
Output:
Overload index
Input:
Power flow data
Fig. 2: Apparent power after a disturbance

## Slide 7: Disturbance Recognition
Functions:
To identify the type of the events by comparing the subspace of online data with the constructed dictionary;
Fig. 3 shows the main idea of our disturbance recognition method.
Input:
Post-event PMU datasets in one second;
Output:
The type of the event.
Fig. 3: Dictionary construction from historical datasets and real-time data identification through subspace comparison